## Slide 1
Status report for the 101 project
Babak Hosseini 30/09/2019
1

## Slide 2
Determining the priority of a failed check based on :
  Check type
  Device name
  Device type (server / workstation)
  Failure detail
  Failure trajectory
….
Master-Vorlage 2019
01.05.2019
Seite 1
Classification task/objective:

## Slide 4
Determining the priority of a failed check based on :
API call → checks status → Priority of the fails → update dashboard
Master-Vorlage 2019
30.09.2019
Seite <number>
Classification task/objective:

## Slide 5
RedMineDB:
Issued tickets related to the past problems
Data is annotated!
!! No direct connection to SolarWinds (mostly)
Mostly created based on the customer calls
Difficult to related to a check in SWs
!! Not all the required detail is always imported
    e.g., device name, device type, Priority
Master-Vorlage 2019
01.05.2019
Seite <number>
Data resources:

## Slide 6
MongoDB:
Record of the past performed checks in SolarWinds (background)
Based on API Calls from SolarWinds  similar to the recall phase
Master-Vorlage 2019
01.05.2019
Seite <number>
Data resources:

## Slide 7
MongoDB:
Record of the past performed checks in SolarWinds (background)
Based on API Calls from SolarWinds  similar to the recall phase
!! Data is not annotated!
!! Large sample time (3 hours)
!! Many of the recorded rows are not necessary!
Passed checks / redundant repetitions
!! Not all the details are clear to the experts
E.g. checkstatus (add, testcleared, testokinactive, etc)
Master-Vorlage 2019
01.05.2019
Seite <number>
Data resources:

## Slide 9
Labeling the failed checks in MongoDB:
Categories (labels):
  High priority failure
  Normal priority failure
  False alarms
  Not enough info is provide
  Monitoring the failure progress
Master-Vorlage 2019
01.05.2019
Seite <number>
Annotation task:

## Slide 10
!! Huge amount of data samples (8M failed checks per month)
Sticking the sequential failure-status together
Reducing from 16M to 5K
Not efficient to do large-scale annotation in a single-run
  Possibility of going wrong esp. at the beginning
  First run: labeling 2 month → google sheet
Master-Vorlage 2019
01.05.2019
Seite <number>
Annotation task:

## Slide 11
Determining the priority of a failed check:
  Based on MongoDB records
  Needs to label the MongoDB data
  A back-and-forth procedure between annotation/classification/data acquisition
  E.g. Annotation A  train classifier  correct annotation A  re-train classifier
 Annotation B  modify/re-train/extend classifier
 re-annotate A
Master-Vorlage 2019
01.05.2019
Seite <number>
Classification-annotation scheme:

## Slide 12
Unbalanced classes
Small H-priority samples compared to other classes
Sparse data samples
  Per type of check (esp. failed cases)
Dis-continues data distribution
Non-numerical features (most cases)
Master-Vorlage 2019
01.05.2019
Seite <number>
Hybrid classification model:

## Slide 13
Checks with priority independent from device or etc.
Hand coded during the annotation phase
Recognized by their constant label in training
e.g. Skriptüberprüfung - Terra Backup → always a critical failure
e.g. Leistungsüberwachung – Prozessorwarteschlange → always can be ignored
e.g. Anti-Virus-Aktualisierungsüberprüfung - Managed Antivirus → cannot be a critical failure ever
Master-Vorlage 2019
01.05.2019
Seite <number>
Hybrid classification model:

## Slide 14
Checks with priority independent from device or etc.
Hand coded during the annotation phase
Recognized by their constant label in training
Checks with priority chosen based on device, extra info, sub-category, etc.
Learned by decision tree
A beforehand feature extraction part
e.g. Festplattenspeicherüberprüfung – Laufwerk → extra info: Frei / Total < 20% → High priority
e.g. PING-Überprüfung – XXX → depends on the device ID XXX
e.g. general pattern of YYY-XXX → classified based on YYY and XXX and other features
Master-Vorlage 2019
01.05.2019
Seite <number>
Hybrid classification model:

## Slide 15
Training: 2 months of checks
Test: 1 month check data
Categories: High priority and non-High priority
Accuracy:
                Class H: 98.4%
                Class nH: 97.4%
                new annotation strategy in favor of class H
Master-Vorlage 2019
01.05.2019
Seite <number>
Classification Result:
 | Class nH | Class H
categorized as nH | 2593 | 69
categorized as H | 7 | 432

## Slide 16
Training: 2 months of checks
Test: 1 month check data
Categories: High priority (H), normal priority (N), false alarm (F)
Accuracy:
                Class H: 98.4 %
                Class N: 94.6%
                Class F: 77.3 %
                Hand-coded rules which
                do not consider false-positives
Master-Vorlage 2019
01.05.2019
Seite <number>
Classification Result:
 | Class N | Class H | Class F
categorized as N | 968 | 52 | 3
categorized as H | 7 | 432 | 0
categorized as F | 355 | 17 | 1267

## Slide 17
Change in the annotation scheme:
New types of check
New sub-categories of checks
Master-Vorlage 2019
01.05.2019
Seite <number>
Classification Issues:

## Slide 18
Change in the annotation scheme:
    Finding new rules  apply to the old annotation
    Manual re-annotation
New types of check
  Training (or hand-coding) a classifier on the data
New sub-categories of checks:
  Re-train the classifier / adding more rules
Master-Vorlage 2019
01.05.2019
Seite <number>
Approaching the Issues:

## Slide 19
Improving the classifier on 1-2 more months of data
Implementing code of API based predictor
SolarWinds API call  check label
Evaluation by 101-team
In-parallel to their own dashboard
Consider it as priority suggestions
Mark the write/wrong prediction (at least for class-H cases)
Master-Vorlage 2019
01.05.2019
Seite <number>
Next phase(s):

## Slide 20
Active learning scheme:
Improve the classifier by new annotations / errors
More data  more complicated models
Temporal analysis of failures
Deep learning frameworks
Master-Vorlage 2019
01.05.2019
Seite <number>
Long-term Plan:

## Slide 21
Connection between RedMine & MongoDB:
More dedication in importing ticket details
  e.g., device name, server/workstation and etc
Relating each ticket to a possible check in SolarWinds
Designing unique checkid for each type of check
where possible
MongoDB (recording API calls)
unique checkid for each type of check
Smarter import intervals depending on the type of check
Master-Vorlage 2019
01.05.2019
Seite <number>
Improvements in the database systems: